## Slide 1: Investigation of the Effect of Axial Ring Splitting for Cost Reduction of Total Body PET Scanners
N. Efthimiou (Univ. of Hull, UK),
S. J. Archibald (Univ. of Hull, UK) and
S. Vandenberghe (Univ. of Ghent, BG)

## Slide 2: Instead of an introduction …
Prof. S. Cherry presented the benefits of the Total body PET scanner.
  Higher sensitivity, real time pharmacokinetics, pediatric imaging
Ass. Prof. S. Surti gave an update on the PENN-PET project
  Modular geometry, current at 700 mm moving to longer geometries.
  Delayed studies
Ms. M. Stockhoff presented the benefits of monolithic detectors in total body PET scanner PET2020.
Each J-PET module has effective length of 50 cm

## Slide 3: Challenges
Large data streams
  Prof. S. Cherry, dr. S. Niedźwiecki
Cost
  Prof. S. Cherry, M. Stockhoff

## Slide 4: Goals
Investigation of the benefits using the split ring geometry.
  Lower cost
Use of open source STIR for reconstruction of long axial FOV scanners
  Processing of large amounts of data

## Slide 5: Simulations
GATE Monte Carlo simulation toolkit
  Adapted NEMA protocol
    The cylindrical phantom was extended to 1.5 m
  XCAT Anthropomorphic phantom
    Normal FDG biodistribution (140 MBq)
    Acquisition of 10 sec in all cases

## Slide 6: Image reconstruction
OSEM - 12 subsets
  2 full iterations (no post-filtering)
  Projection data reconstruction
  No Time-Of-Flight
  No axial compression
  No views mashing
  No scattered or random photons were considered
Maximum acceptance angle ~27deg (Segment num range ≤(-167, 167)
Reconstruction performed on cluster, with OpenMP (32 cores)
  No GPU

## Slide 7: 1. Split rings geometry

## Slide 8
Stefaan Vandenberghe, UGhent

## Slide 9: Implementation of split rings in GATE
Each detector block had 8x8 LYSO crystals (4.07 mm)
In GATE the shift or Rsectos (± 16.5 mm) was used.
Then the ring was repeated 10 times

## Slide 10: Counting performance
Prompts NECR

## Slide 11: 2. PENN-PET based modifications

## Slide 12: PENN-PET based geometry
* I. Rauschet al., “Performance Evaluation of the Vereos PET/CTSystem According to the NEMA NU2-2012 Standard,”J. Nucl. Med.,vol. 60, no. 4, pp. 561–567, Apr. 2019.DOI: 10.2967/jnumed.118.215541

## Slide 14: Performace
~7 mm radial spatial
Resolution
~8 mm axial resolution

## Slide 15
Num. Det. Rings: 1
Num. Of rings: 56
Full iteration: ~0.5 h
Data min: 0
Data max: 6
Data sum: 1.85165e+07
Num Det. Rings: 3
Num. Of rings: 168
Full iteration: ~1.1 h
Data min: 0
Data max: 6
Data sum: 9.54506e+07
Num. Det. Rings: 3
Num. Of rings: 224
Full iteration: ~7. h
Data min: 0
Data max: 7
Data sum: 7.76138e+07
https://github.com/UCL/STIR

## Slide 17: Going longer …
Num. Det. Rings: 5
Num. Of rings: 280
Full iteration: 3.5 h
Data min: 0
Data max: 6
Data sum: 1.30175e+08
Num. Det. Rings: 8
Num. Of rings: 448
Full iteration: 8 h
Data min: 0
Data max: 5
Data sum: 1.30998e+08

## Slide 18
I would like to thank:
  Dr. Assem Allam, Fatima Allam and the Allam Family.
  Prof. S.J. Archibald
  UCL:
    Prof. K. Thielemans
  UoLeeds:
    P. Wadhwa
    M. Oloniyo
    dr. C. Tsoumpas