## Slide 1: Ortho-Positronium Detection with a High-Resolution PET Scanner
Firas Abouzahr
University of Texas at Austin
Department of Physics
July 5th, 2024

## Slide 2: Time-of-Flight PET for Proton Therapy (TPPT)
3 x 3 x 15 mm3 LYSO (Lu1.8Y0.2SiO5:Ce) Crystals
Hamamatsu S14161-3050HS-08 silicon photomultiplier (SiPM) [1]
One-to-one coupling between scintillator and SiPM pixels
6144 total detector channels  3072 per crescent.
SiPM channel readout and DAQ provided by PETSys Electronics [2]

## Slide 3: TPPT Research PET Scanner Metrics
Initial measurements yield ~2 mm spatial resolution.
Optimized timing resolution < 200 ps
~6.5% energy resolution at 0.511 MeV
CTR = 180 ps
Eres = 6.5%

## Slide 4: Ortho-Positronium (o-Ps): Why Three Photons?
Coupled spins of ground-level fermion-antifermion state:
S = || , … , || = |½ +½ |, … , |½ - ½ | = 0,1
In the basis of for Spin-1, we get a triplet state (o-Ps):
The Charge Conjugation (C) operator acting on a on photon:
C | = -1 |
C |n = (-1)n |
C operating on a fermion-antifermion bound state:
C| = (-1)L+S |
C| = (-1)0+1 | = -1 |
C symmetry in EM interactions demands n be odd (n≠1) for o-Ps → n𝛾.
3𝛾 (n = 3) occurs with highest probability. 0.5% - 1.5% of total events.
e-
e+
e-
e+
Spin-1
(Ortho-Positronium)
Spin-0
(Para-Positronium)

## Slide 5: Experimental Setup
26 mm
3.2 mm
Na-22 (~4.5 µCi)
Experimental setup:
Na-22 Button source placed in isocenter of PET scanner.
Only 30-minute data acquisition!
PMMA case acts as medium for Ps formation.
Source placed horizontally to maximize formation area.
Data processed into triple coincidences to search for o-Ps → 3𝛾
e+
e-
Figure taken from https://physicsopenlab.org/2016/05/22/webcam-particle-detector-measurements/

## Slide 6: Geant4 Simulations
o-Ps single photon energy spectrum as predicted by nrQED
TPPT research PET scanner in GEANT4

## Slide 7: Geant4 Simulations
o-Ps single photon energy spectrum as predicted by non-relativistic quantum electrodynamics [3].
Figure taken from D. Kaminska et al (2016) [4]

## Slide 8
1. True event: o-Ps→3𝛾 and all three photons interact. *
Triple Coincident Events
Annihilation Gammas
Scattered Gammas
Prompt Gammas
* Also, o-Ps events where a photon misses but scattering adds a third signal.

## Slide 9
Triple Coincident Events
Annihilation Gammas
Scattered Gammas
Prompt Gammas
1. True event: o-Ps→3𝛾 and all three photons interact. *
* Also, o-Ps events where a photon misses but scattering adds a third signal.
2. False event: Back-to-back photons interact + a Compton Scatter

## Slide 10
2. False event: Back-to-back photons interact + a Compton Scatter
Triple Coincident Events
Annihilation Gammas
Scattered Gammas
Prompt Gammas
3. False event: Two photons interact (either back-to-back or from o-Ps) + contribution by Prompt gamma.
1. True event: o-Ps→3𝛾 and all three photons interact. *
* Also, o-Ps events where a photon misses but scattering adds a third signal.

## Slide 11
Triple Coincident Events
* Also, o-Ps events where a photon misses but scattering adds a third signal.
Annihilation Gammas
Scattered Gammas
Prompt Gammas
4. False Event: Coincidence window allows for photons from different events to be counted as coincident.
1. True event: o-Ps→3𝛾 and all three photons interact. *
2. False event: Back-to-back photons interact + a Compton Scatter
3. False event: Two photons interact (either back-to-back or from o-Ps) + contribution by Prompt gamma.

## Slide 12: Filtering Techniques
Energy
2. Decay Plane Cut
4. Time-of-Flight
3. Momentum Conservation
Θ12
Θ23
Θ13
∆T
1.5σ cut below on the photopeak
1.022 MeV cut

## Slide 13: Filtering Techniques
Energy
2. Decay Plane Cut
4. Time-of-Flight
3. Momentum Conservation
Θ12
Θ23
Θ13
∆T
1.5σ cut below on the photopeak
1.022 MeV cut
Filtering techniques inspired by the pioneering work of J-PET [5]

## Slide 14: Momentum Conservation
Define Θ12 < Θ23 < Θ13 between momentum vectors:
If Θ12 + Θ23 < 180˚ then Θ13 > 180˚.
If Θ12 + Θ23 > 180˚ then Θ13 < 180˚.
Θ12
Θ23
Θ13
Momentum not conserved
❌
Θ12
Θ23
Θ13
Momentum conserved
✅

## Slide 15: Momentum Reconstruction in Geant4: 2𝛾 Events
Event Diagnosis:
Event Diagnosis:
Event Diagnosis:
Event Diagnosis:
Back-to-back gamma deposition + Compton Scattering.
Event Diagnosis:
Prompt gamma acts as third signal in triple coincidence

## Slide 16: Momentum Reconstruction in Geant4: 3𝛾 Events
Event Diagnosis:
Event Diagnosis:
Event Diagnosis:
Event Diagnosis:
Two of three photons interact + Compton Scattering.
Geometric constraint of crescent geometry.
Event Diagnosis:
Prompt gamma acts as third signal in triple coincidence

## Slide 17: Momentum Reconstruction
Observations in experimental data:
Broadening of the back-to-back gamma line at 180˚
Additional ”noise” across the entire spectrum.
Potential o-Ps→3𝛾 candidate region (Θ12 + Θ23 ≥ 186˚)
Assumed f3𝛾 = 0.5%

## Slide 18: Time-of-Flight + Control Study
Monte Carlo result does not tell the whole story… it does not *yet* account for timing.
True triple coincident photons should be detected in very close temporal proximity.

## Slide 19: Time-of-Flight + Control Study
As a control study, the same filtering pipeline was applied to data acquired from a steel encased Ge-68.
Within metals we expect to observe few 3𝛾 events.
We see an evident quenching effect in the metal, further validating the observation of o-Ps→3𝛾 events in our plastic casing.
The number of potential o-Ps→3𝛾 candidates changes as we vary the required detection time window.
Monte Carlo result does not tell the whole story… it does not *yet* account for timing.
True triple coincident photons should be detected in very close temporal proximity.

## Slide 20: Conclusion & Next Steps
We have seen strong evidence of o-Ps→3𝛾 events from Ps formation in the plastic of a Na-22 button source using our research PET scanner. ~ with a non-optimized experiment.
The result follows from guidance by Geant4 simulations & employing four techniques to remove false triples:
  Energy – photopeak and 1.022 MeV cuts
  Decay plane cut
  Timing
  Conservation of Momenta
A control study done with metal encased Ge-68 illustrates the expected quenching of 3𝛾 events compared to the plastic Na-22 study.
Next steps:
Optimize experimental setup to boost f3𝛾 (aerogels).
Lifetime measurements.
Positronium in conventional and FLASH proton therapy.

## Slide 21: Dziękuję za uwagę
Acknowledgements
University of Texas at Austin
Department of Physics
UTKL Group :
Prof. Karol Lang (P.I)
John Cesar Ph.D.
Marek Proga
Michael Gajda
Alex Kuo
Aryan Ojha
Laboratory of Instrumentation and Experimental Particle Physics
University of Coimbra, Portugal
Andrey Morozov Ph.D.

## Slide 22
References
[1] Hamamatsu silicon photo-multipliers(SiPM), or mult-pixel photon counters(MPPC). Hamamatsu Photonics K. K, Hamamatsu City, Japan.
[2] PETSys Electronics S.A., Taguspark, Ed. Tecnologia I, 24 and 26, 2740-257, Portugal.
[3] Ore, A., & Powell, J. L. (1949). Three-photon annihilation of an electron-positron pair. Physical Review, 75(11), 1696.
[4] Kamińska, D., Gajos, A., Czerwiński, E., Alfs, D., Bednarski, T., Białas, P., ... & Moskal, P. (2016). A feasibility study of ortho-positronium decays measurement with the J-PET scanner based on plastic scintillators. The European Physical Journal C, 76, 1-14.
[5] Dulski, K., Bass, S. D., Chhokar, J., Chug, N., Curceanu, C., Czerwiński, E., ... & Moskal, P. (2021). The J-PET detector—a tool for precision studies of ortho-positronium decays. Nuclear Instruments and Methods in Physics Research Section A: Accelerators, Spectrometers, Detectors and Associated Equipment, 1008, 165452.

## Slide 23: Back-up Slides

## Slide 24: Photopeak Normalization and Alignment
SiPM channels are not yet energy calibrated.
First order energy approximation from DAQ Unit.
DAQ units are sufficient for double coincidences… but known energy values are needed in triple events.
Fix title

## Slide 25: Energy Cut
Two Energy Cuts:
Filter out triple coincidences that do not meet Etotal = 1.022 ± 0.1 MeV
1.5σ cut below the photopeak to remove known back-to-back & prompt gamma depositions.
Prompt
Gammas

## Slide 26: Simulated Energy Spectra